## Slide 1: PlaatProtect (Burglar / Fire Alarm Centre) Open Source Project
W.B.J. van der Plaat
(Principal IT Architect)

## Slide 2: Questions
How can I protect my family and house against burglars?
How can I protect my family and house against fire?

## Slide 3: Idea
Lets create an application which detect movement & fire in my house and activate the necessary counter measure(s).
Web Gui
Use low cost hardware
Use Z-Wave technology
Use Zigbee technology

## Slide 4: PlaatProtect - Features
Burglar / Fire Alarm Centre on Raspberry Pi
  Integrate Webcams
    Motion detection with auto recording
  Integrate Z-Wave meshwork
    IR detector(s)
    Alarm Horn
  Integrate Zigbee meshwork
    Control lights
    Fire detector
  Notification
    Push Message to Mobile
    Email
  Scenario support
    Home, Sleep, Away

## Slide 5: PlaatProtect Software Architecture
REST
Interface
Zigbee
Interface
Z-Wave
Interface
Webcam
Interface
Database Layer
Business Logic Layer
Presentation Layer
Google Charts
Email Push Service
WS/JSON/JS
PHP/CSS/JS
PHP
MySQL
PHP
Operating
System
Debian Linux
Vendor Support
Philips HUE
Vendor support
Google Protect
Vendor support
Sony
Logitec
Vendor support
- Aeotec
- Aeon
Apache
Mobile Push Service

## Slide 6: Information Exchange
GUI
Process Event Handler
Webcam
Interface
Z-Wave
Interface
Zigbee
Interface
Android Notification
Email
Interface
Service
Bus
(Implemented in
Database)
json
json
json
json
json
json
files
Directory
files

## Slide 7: Used hardware
Raspberry Pi 3B
Philips Hue Light Bulb
Philips Hue Light Strip
Z-Wave USB Dongle
Z-Wave Aeon Horn
Z-Wave Aeotec IR detectors
Google Nest Protect
USB Webcam

## Slide 8
Raspberry Pi
PlaatProtect
Sense Hat (Pi)
Wifi Router
Webcam
1
ADSL Router
Internet
USB
USB
Z Wave
(mesh network)
Ethernet
Webcam
2
IR
Detector
Alarm
Horn
Wifi
Notification
USB
Ethernet
Ethernet
Zigbee
(mesh network)
Light
Bulb
Light
Strip
Hardware View – Configuration 1
Fire
Detector

## Slide 9
Raspberry Pi
PlaatEnergy
PlaatProtect
Sense Hat (Pi)
Solar
Converter
Digital Energy
Meter
Digital Gas
Meter
Wifi Router
P1 cable
Webcam
1
Wifi
Bluetooth
ADSL Router
Internet
USB
USB
Z Wave
(mesh network)
Ethernet
Webcam
2
Wifi
USB
Ethernet
Ethernet
Zigbee
(mesh network)
Light Bulb
Light
Strip
USB
Hardware View – Configuration 2
Notification
Z Wave
(mesh network)
IR
Detector
Alarm
Horn
Fire
Detector

## Slide 10: Scenario – Home
IR
Detector
PlaatProtect
Light
Bulb
Movement
Alarm
Activate
Bulb
Event
Data
Cloud Storage

## Slide 11: Scenario – Sleep
PlaatProtect
Light Bulbs
Movement
Or
Vibration
Alarm
Activate
some
Light Bulbs
IR
Detector
IR
Detector
IR
Detector
IR
Detector
Webcam
Webcam
Movement
Detected
Horn
Activate
Horn
Cloud Storage
Video
Stream
Event
Data

## Slide 12: Scenario – Away
IR
Detector
PlaatProtect
Activate
all
Light Bulbs
IR
Detector
IR
Detector
IR
Detector
Send
push message
to mobile(s)
Send
Email
Activate
Horn
Webcam
Webcam
Bulb Lights
Mobile
Horn
Email
Movement
Or
Vibration
Alarm
Activate Drone
“Search and …..”
PiZorg
Movement
Detected
TOP
SECRET
Video
Stream
Cloud Storage
Event
Data

## Slide 18: Conclusion
My family and house are “better” protected against burglars
One burglar attempt in my street captured on video and shared with Police 
Learned a lot about Z-Wave protocol. Z-Wave protocol specification is not public 
Google Nest Protect Zigbee integration not possible. Only web service integration possible 
Learned a lot about basic video motion detection

## Slide 19
IR
Detector
More info
visit
plaatsoft.nl